## Slide 1: Mahavir Education Trust’s Shah & Anchor Kutchhi Engineering College Chembur, Mumbai-400088 (An Autonomous Institute Affiliated to University of Mumbai)
Department of Cyber Security
presentation
on
Multilayer Switches
(Subject: Operating Systems, CSCOR1PC201, III Semester)

## Slide 2: Vision & Mission
To become a globally recognized institution offering quality education and enhancing professional standards
To impart high quality technical education to the students by providing an excellent academic environment, well - equipped laboratories and training through motivated teachers.
Institute Vision
1. To deliver high-quality cybersecurity value-based education and enhancing the teaching-learning process for professional excellence.
2. To promote research, industry collaboration and entrepreneurship to address global challenges in cybersecurity.
To be a globally recognized department that provides quality education in cybersecurity, promotes ethical practices, and prepares professionals to tackle real world challenges.
Institute Mission
Department Vision
Department Mission

## Slide 3: Program Specific Outcomes
Index | Outcome
PSO1 | Cybersecurity graduates will understand evolving threats and vulnerabilities in both software and hardware within the field of cybersecurity.
PSO2 | Cybersecurity graduates will demonstrate the ability to ethically use tools and technologies to develop innovative solutions while balancing security, privacy, and law enforcement needs.

## Slide 4: Outline
Prepare an 8–10 slide PowerPoint presentation covering:
Title
Problem Statement
Background
Working Principle
Architecture / Diagram
Demonstration
Real-Time Application
SDG Mapping
Conclusion
References

## Slide 5
Multilayer Switches in Data Centers
A High-Speed Solution for Inter-VLAN Routing and Network Performance
COMPUTER NETWORKS
CISCO PACKET TRACER
Made by Stuti Shah
SYCS_53
PRN: 125BTCS1057

## Slide 6
The Problem We're Solving
The Challenge
Modern data centers require high-speed communication between multiple departments while maintaining security and scalability. Traditional Layer 2 switches cannot route traffic between VLANs, and deploying separate routers introduces cost, complexity, and latency.
Project Objective
Design, analyze, and demonstrate a multilayer switching solution that delivers efficient Inter-VLAN Routing with improved performance, scalability, and security — all within a single device.

## Slide 7
What Is a Multilayer Switch?
A multilayer switch combines Layer 2 and Layer 3 functionality in one device — eliminating the need for a separate router in many enterprise scenarios.
Layer 2 Switching
Forwards frames based on MAC addresses within the same VLAN.
Layer 3 Routing
Routes packets using IP addresses across different
VLANs.
Inter-VLAN Routing
Enables communication between VLANs without an external router.
Hardware-Based
ASIC-based forwarding delivers wire-speed performance.

## Slide 8
Working Principle
When a packet arrives, the multilayer switch inspects both the MAC and IP addresses to determine whether to
switch or route.
Forward to VLAN
Layer 3 Route
Inspect MAC & IP
Device Sends
If the destination is local, the frame is switched at Layer 2. If it belongs to another VLAN, the switch routes it through the appropriate Switch Virtual Interface (SVI).

## Slide 9
Network Architecture
Cisco 3560 Multilayer Switch
The switch acts as the central routing and switching hub. Each VLAN has a dedicated Switch Virtual Interface (SVI) that serves as the default gateway for all devices in that VLAN.
VLAN 10 — PC1 (192.168.10.10), Gateway: 192.168.10.1
VLAN 20 — PC2 (192.168.20.10), Gateway: 192.168.20.1
VLAN 30 — Server (192.168.30.10), Gateway: 192.168.30.1
IP Routing must be explicitly enabled on the switch for
Inter-VLAN communication.

## Slide 10
Practical Demonstration
Using Cisco Packet Tracer, the following configuration was implemented and verified step by step.
01
Create VLANs 10, 20, and 30
Defined VLANs on the Cisco
3560 switch.
02
Assign Switch Ports
Assigned access ports to each
VLAN.
03
Configure SVIs
Created Switch Virtual Interfaces with IP addresses as default gateways.
04
Enable IP Routing
Activated Layer 3 routing with ip routing.
05
Verify with Ping
Confirmed successful Inter-VLAN communication between all devices.

## Slide 11
Real-World Applications
Multilayer switches are deployed wherever high-performance, segmented networking is required.
Enterprise Networks
Connect departments securely while maintaining performance.
Data Centers
Route traffic between server VLANs at wire speed.
Campus & Universities
Segment academic, administrative, and guest networks.
Hospitals & Cloud
Isolate critical systems and support cloud infrastructure.

## Slide 12
Alignment with Sustainable
Development Goals (SDG)
Why This Matters
This project connects networking education and practice to broader global goals — demonstrating that technical solutions can drive social and economic progress.

## Slide 13
Conclusion
Unified Functionality
Combines Layer 2 switching and Layer 3 routing in a single device — no external router required.
High-Speed Inter-VLAN Routing
Hardware-based routing dramatically reduces latency compared to router-on-a-stick designs.
Scalable & Secure
VLAN segmentation with SVI-based routing supports growing enterprise and data center environments.
Proven in Simulation
Cisco Packet Tracer successfully demonstrated end-to-end Inter-VLAN communication across three VLANs.

## Slide 14
References
1
Cisco Networking Academy
Switching, Routing and Wireless Essentials
2
Cisco Catalyst 3560 Guide
Official Configuration Guide
3
Cisco Packet Tracer
User Guide and Simulation Platform
4
Kurose & Ross
Computer Networking: A Top-Down Approach
5
Cisco Learning Network
VLANs and Inter-VLAN Routing Resources
All configurations and demonstrations were validated using Cisco Packet Tracer in alignment with Cisco
Networking Academy curriculum standards.

## Slide 15
Thank You